Instruction : Adjustable spacer:

Track clamps for laying parallel tracks

Two adjustable clamps (similar to those above) are mounted on a brass rod which has a scale marked on it.

This allows the tracks to be laid at a constant parallel distance of between 32 mm and 60 mm. The clamps are held in positions on the rod by knurled wheeled screws, and the clamps may be moved in the vertical plane to allow fore use on cambers. The clamps  may also be removed from the rod and used separately.

Method of use:

1.  Loosen the screws on BOTH Clamps

2.  Loosen the retaining screw to move the first clamp to the required setting on the scale, and then re-tighten. Place this clamp on the first piece of track.

3.  Move the second clamp to the desired position on the scale and tighten the wheel.

4.  Place  the second piece of track so that the second clamp sits between the rails, and tighten this clamp also

Now the track will automatically maintain the correct parallel distance when the clamps are moved along it.